## Slide 1: Smart Card Contact based communication protocol Basics
Amritraj Ugranimane (IFIN CCS TI SWP)
19-Jan-2018

## Slide 2: Agenda
Basic Startup sequence
APDU Cases
APDU vs TPDU
Importance of Procedure Bytes
T=0 Protocol and its TPDU’s
T=1 Protocol and its TPDU’s

## Slide 3: Basic Start-up Sequence
Reset
ATR
PPS Request
PPS Response
APDU Command
APDU Response
Terminal
Card

## Slide 4: PPS –Protocol and Parameter Selection
PPSS | PPS0 | PPS1 | PPS2 | PPS3 | PCK
PPSS | PPS0 | PPS1 | PPS2 | PPS3 | PCK
PPS Request
PPS Response
Terminal
Card
 |  | Higher Nibble |  | Lower Nibble
 |  | b8 to b5 |  | b4 to b1
PPSS | Mandatory | FF |  | 
PPS0 | Mandatory | P/A | T (Protocol | 
PPS1 | Optional | F/D (Baudrate) |  | 
PPS2 | Optional | RFU |  | 
PPS3 | Optional | RFU |  | 
PCK | Mandatory | Checksum |  | 

## Slide 5: APDU Command Response Pair
APDU Request
APDU Response
Terminal
Card
CLA | INS | P1 | P2 | Lc | Command Data | Le
Response Data | SW1 | SW2
 | Cmd Data | Resp Data
Case 1 | 0 | 0
Case 2 | 0 | 1
Case 3 | 1 | 0
Case 4 | 1 | 1
Legends | 
0 | Absent
1 | Present
Header

## Slide 6: APDU Cases
CLA | INS | P1 | P2 | Le
CLA | INS | P1 | P2 | Lc | Command Data
CLA | INS | P1 | P2
Terminal
Card
SW1 | SW2
Response Data | SW1 | SW2
SW1 | SW2
Response Data | SW1 | SW2
CLA | INS | P1 | P2 | Lc | Command Data
Case 1
Case 2
Case 3
Case 4

## Slide 7: APDU vs TPDU
APDU - Application Protocol Data Unit
TPDU – Transport Protocol Data Unit
Application Layer
Transport Layer
Physical Layer
Application Layer
Transport Layer
Physical Layer
Card
Terminal
APDU
TPDU
IO Line
Communication Channel

## Slide 8: Procedure Bytes
Instruction Byte
Inverse Instruction Byte (Deprecated)
Wait Extension (60)
6X or 9X except 60
INS
Null
SW1
INS

## Slide 9: T=0 Case 1 TPDU
Terminal
Card
SW1 | SW2
CLA | INS | P1 | P2 | P3 = 00

## Slide 10: T=0 Case 3 TPDU
Terminal
Card
SW1 | SW2
CLA | INS | P1 | P2 | Lc
INS
Command Data

## Slide 11: T=0 Case 2 TPDU
Terminal
Card
INS | Response Data | 90 | 00
Le = Lr
INS | Response Data (Le) | 61 | Lr-Le
Le < Lr
CLA | INS | P1 | P2 | Le
INS | Response Data (Lr-Le) | 90 | 00
00 | C0 | 00 | 00 | Lr-Le
Le > Lr
CLA | INS | P1 | P2 | Le
INS | Response Data (Lr) | 90 | 00
CLA | INS | P1 | P2 | Lr
6C | Lr
CLA | INS | P1 | P2 | Le

## Slide 12: T=0 Case 4 TPDU
Terminal
Card
CLA | INS | P1 | P2 | Lc
61 | XX
INS
Command Data
Le = Lr
Le < Lr
Le > Lr
Get Response follows
With case 2 handling

## Slide 13: T=1 Protocol
Block based protocol
Prologue |  |  | Information | Epilogue
NAD | PCB | LEN | INF | EDC
1 Byte | 1 Byte | 1 Byte | 0 to 254 Bytes | 1 or 2 Bytes

## Slide 14: T=1 scenarios

## Slide 15: T=1 scenarios continued

## Slide 16: T=1 scenarios continued